## Slide 1
Computer System Architecture
Boolean Algebra
Nitesh Kumar
200104@cs.du.ac.in

## Slide 2: Learning Objectives
In this you will learn about:
Boolean algebra
Fundamental concepts and basic laws of Boolean algebra

## Slide 3: Boolean Algebra
An algebra that deals with binary number system
George Boole (1815-1864), an English mathematician, developed it for:
  Simplifying representation
  Manipulation of propositional logic
In 1938, Claude E. Shannon proposed using Boolean algebra in design of relay switching circuits
Provides economical and straightforward approach
Used extensively in designing electronic circuits used in computers

## Slide 4: Fundamental Concepts of Boolean Algebra
Use of Binary Digit
  Boolean equations can have either of two possible values, 0 and 1
Logical Addition
  Symbol ‘+’, also known as ‘OR’ operator, used for logical addition. Follows law of binary addition
Logical Multiplication
  Symbol ‘.’, also known as ‘AND’ operator, used for logical multiplication. Follows law of binary multiplication
Complementation
  Symbol ‘-’, also known as ‘NOT’ operator, used for complementation. Follows law of binary compliment

## Slide 5: AND OR

## Slide 6: Operator Precedence
Each operator has a precedence level
Higher the operator’s precedence level, earlier it is evaluated
Expression is scanned from left to right
First, expressions enclosed within parentheses are evaluated
Then, all complement (NOT) operations are performed
Then, all ‘’ (AND) operations are performed
Finally, all ‘’ (OR) operations are performed

## Slide 7
1st
2nd
3rd
X  Y  Z

## Slide 8: Postulates of Boolean Algebra
Postulate 1:
A = 0, if and only if, A is not equal to 1
A = 1, if and only if, A is not equal to 0
Postulate 2:
x  0 = x
x  1 = x
Postulate 3: Commutative Law
x  y = y  x
x  y = y  x

## Slide 9: Postulates of Boolean Algebra
Postulate 4: Associative Law
(a) x  (y  z) = (x  y)  z
(b) x  (y  z) = (x  y)  z
Postulate 5: Distributive Law
(a) x  (y  z) = (x  y)  (x  z)
(b) x  (y  z) = (x  y)  (x  z)
Postulate 6:
x + x = 1
x  x = 0

## Slide 10: The Principle of Duality
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
 | Column 1 | Column 2 | Column 3
Row 1 | 1  1 = 1 | 1 + 0 = 0  1 = 1 | 0  0 = 0
Row 2 | 0  0 = 0 | 0  1 = 1  0 = 0 | 1  1 = 1
There is a precise duality between the operators (OR), and the digits 0 and 1.
. (AND) and +
For example, in the table below, the second row is obtained from the first row and vice versa simply by interchanging ‘+’ with ‘.’ and ‘0’ with ‘1’
Therefore, if a particular theorem is proved, its dual theorem automatically holds and need not be proved separately

## Slide 11: Some Important Theorems of Boolean Algebra
Sr. No. | Theorems/ Identities | Dual Theorems/ Identities | Name (if any)
1 | x + x = x | x  x = x | Idempotent Law
2 | x + 1 = 1 | x  0 = 0 | 
3 | x + x  y = x | x  x + y = x | Absorption Law
4 | x = x |  | Involution Law
5 | x  x + y = x  y | x +x  y = x + y | 
6 | x y = x y  | x  y = x y+ | De Morgan’s Law

## Slide 12: Methods of Proving Theorems
The theorems of Boolean algebra may be proved by using
one of the following methods:
By using postulates to show that L.H.S. = R.H.S
By Perfect Induction or Exhaustive Enumeration method where all possible combinations of variables involved in
L.H.S. and R.H.S. are checked to yield identical results
By the Principle of Duality where the dual of an already proved theorem is derived from the proof of its corresponding pair
80

## Slide 13: Proving a Theorem by Using Postulates (Example)
Theorem:
x + x · y = x
80
Proof:
L.H.S.
= x  x  y
= x  1  x  y
= x  (1  y)
= x  (y  1)
= x  1
= x
= R.H.S.
by postulate 2(b) by postulate 5(a) by postulate 3(a) by theorem 2(a) by postulate 2(b)

## Slide 14: Proving a Theorem by Perfect Induction (Example)
Theorem:
x + x · y = x
=
x | y | x  y | x  x  y
0 | 0 | 0 | 0
0 | 1 | 0 | 0
1 | 0 | 0 | 1
1 | 1 | 1 | 1

## Slide 15: Proving a Theorem by the Principle of Duality (Example)
Theorem:
x + x = x
Proof:
L.H.S. |  | 
= x  x |  | 
= (x  x)  1 |  | by postulate 2(b)
= (x  x)  (x + | X) | by postulate 6(a)
= x  x  X = x  0 = x = R.H.S. |  | by postulate 5(b) by postulate 6(b) by postulate 2(a) (Continued on next slide)
80

## Slide 16: Proving a Theorem by the Principle of Duality (Example)
Dual Theorem:
x  x = x
Proof:
80
L.H.S.
= x  x
= x  x  0
= x  x  x X
= x  (x + X )
= x  1
= x
= R.H.S.
by postulate 2(a) by postulate 6(b) by postulate 5(a) by postulate 6(a) by postulate 2(b)
Notice that each step of the proof of the dual theorem is derived from the proof of its corresponding pair in the original theorem

## Slide 17: Boolean Functions
A Boolean function is an expression formed with:
  Binary variables
  Operators (OR, AND, and NOT)
  Parentheses, and equal sign
The value of a Boolean function can be either 0 or 1
A Boolean function may be represented as:
  An algebraic expression, or
  A truth table
80